## Slide 1: AXELプロジェクト
A.K.Ichikawa, Kyoto university
for the AXEL collaboration

## Slide 2: AXEL group
A. K. Ichikawa (Kyoto)
Ki. Nakamura (Kobe,PD)
S. Ban (Kyoto,D2)
M. Yoshida (Kyoto, M2)
Ka. Nakamura(Kyoto,M2)
S. Tanaka (Kyoto,D1)
上島考太(東北大RCNS)、関谷洋之(東大宇宙線研)、中島康博(東大宇宙線研)、中家剛(京大)、廣瀬昌憲（京大）、身内賢太朗(神戸大)、南野彰宏氏(横国大)

## Slide 3: neutrino-less double-beta () decay
happens if neutrino is its own anti-particle (Majorana type) and has Mojorana mass components.
Next generation experiments are aiming to cover here, but…
  Life time
Need > 1 ton double-beta nuclei
10meV
J.Shirai, Neutrino2016

## Slide 4: Keys for decay search and our approach
Qbb
Arbitrary scale
Large Mass
High energy resolution
background rejection
  abundance : 8.9%
  MeV
Semiconductors, bolometers and
Ionization of noble gas!
tracking detectors

## Slide 5: High Energy resolution by Xenon proportional scintillation mode (Electroluminescence from ionization electrons)
W-value 21.5 eV, Fano factor<0.17
  0.29%(FWHM)@2.48MeV
  comparable to semi-conductors!
  c.f. Ge 0.2%, EXO 3%, KamLand-Zen 9%
At higher density, energy resolution becomes worse.
  reject liquid option.
Proportional Scintillation mode using electroluminescence lights
  linear process Good linearity and stability
  #photons ∝ voltage drop rather than the field strength.
There is already pioneering work by D.Nygren and the NEXT collaboration
0 1 2 3 4
Density g/cm3
A. Bolotnikov, B. Ramsey Nucl. Instr. And Meth. A396(1997) 360
Energy Resolution %
0 2 4 6 8
Eg=662keV
100bar
e
atom
photon
electroluminescence

## Slide 6: What we propose in the AXEL project
136Xe ~10bar ~1ton
ELCC plane
PMT
~2m
MPPC
electrode w/ hole
mesh
PTFE
w/ holes
anode
Mesh electrode
MPPC photon sensor array
e
atom
photon
electroluminescence process
Linear multiplication process
High energy resolution
(goal: <0.5%(FWHM))
Background rejection by event topology
Electro luminescence light collection cell (ELCC)

## Slide 7: Why ELCC?
PMT
Usually, photo sensor arrays and meshes are used.
Then acceptance to EL photon changes depending on the EL gen. position.  worsen energy resolution
Case : sensors are placed very close to meshes.
Case : sensors are placed far end to meshes.
MPPC
mesh

## Slide 8: ELCC -ElectroLuminescence Light Collection Cell -
MPPC
Line of electric force
electrode w/ hole
mesh
anode
PTFE w/ holes(~f5mm)
Mesh electrode
MPPC photon sensor array
MPPC
CELL pitch 7.5mm~15mm
Uniform response in wide area
extendable to large size with the rigid structure

## Slide 9: AXEL -Expected event topologies-
0nbb a Compton g
10cm
10cm
10cm
simulation
10atm, 15mm pitch, 1ms sampling (~1mm)

## Slide 10: (very) rough sensitivity estimation for 1-ton detector
10bar 1ton enriched 136Xe
Signal
  a few events/year @ =20meV
  - 79% contained in fiducial volume
  - 49% after clustering
  - 22% after blob-recognition
Background
  Only 214Bi considered now. (cannot be separated by E)
  10 ton low background(3ppb) material
  - 12k evts/yr in fiducial
  - 75 evts/yr after clustering
  7 evts/yr w/ blob-recognition
  considering thin vessel in pressurized wator
  - 0.1 evts/yr
Recognition of track with a blob at both ends.
(algorithm optimization still in progress)

## Slide 11
Measure recombination rate by comparing scintillation yield and ionization yield
Observed in Xe+TMA for (D.C.Herrera et al. 2015 Proc. of Sci. TIP2014 057), but scintillation suppressed.
別の方法を模索中
  磁場をかけたがうまくいかなかった。今は、別の方法でデータ取得中

## Slide 12: comments & timeline
ELCCの原理検証は、かなりできた。
近々の課題
  高電圧をてなづける
  コストダウン
  次の予算獲得
スケジュールの目標
  2017-2017: 180L検出器 キセノン量 8.6kg @ 9気圧, 1146ch
    1.8MeVで性能実証
  2017?~2020? : 2,000L検出器 phase 0, キセノン量 100kg@9気圧,約6,000ch
  2020? - : 2,000L検出器に136Xeを入れて世界記録更新を目指す
  202? - 1トン検出器製作に着手。
20 meV、そしてその先に行くには、もう一ひねり必要。
  いくつかアイデアはあり。ただし、もちろんstraight forwardではない。が、なんとか、もう一アイデアものにしたい。