## Slide 1: High pressure Xe gas TPC for 0νββ decay search :
Sei Ban
Kyoto University
For the AXEL collaboration

## Slide 2
AXEL experiments
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Future prospect
Summary
Contents
DBD18
21 Oct 2018

## Slide 3
AXEL experiments
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Future prospect
Summary
Contents
DBD18
21 Oct 2018

## Slide 4
High pressure Xe gas TPC with unique cell readout structure
for 0νββ decay search
136Xe 10 bar
ELCC plane
150~200kV
PMT
e
Atom
photon
Linear response to applied electric field
Without avalanche process
→ less fluctuation of multiplication
Details are in the next page
  ● Electroluminescence (EL) process
Readout Ionization signals
Large mass
→ ton scale 136Xe gas
→ goal : 0.5%FWHM @ Q-value
Φa few meters
a few meters
Scintillation
Ionization
electrons
Good energy resolution
Tracking
(BG rejection)
A Xe ElectroLuminescence : AXEL
DBD18
21 Oct 2018

## Slide 5
Electroluminescence Light Collection Cell : ELCC
- Energy measurement and Tracking in each cells
- Uniform response to event position
- Extendable to large size because of its rigid structures
EDrift
MPPC
MPPC
MPPC
EEL
e-
e-
e-
e-
Ionization electrons are collected into cells
if EEL > EDrift , And converted into EL light
Simulation study of ELCC was done and presented
in XeSAT2017
( https://indico.cern.ch/event/573069/sessions/230066/attachments/1440275/2217034/kisekinakamura_20170405_XeSAT.pdf )
A Xe ElectroLuminescence : AXEL
DBD18
21 Oct 2018

## Slide 6
expected event displays
(simulation : 10 atm Xe, 15mm-pitch, 1MHz sampling)
0nbb
a-ray (2.5MeV)
Compton g-ray (2.5MeV)
simulation
Reconstruct the event topologies from
hit pattern and wave form
- α and multi-site events are easily removed
- Photo absorption of gamma events are
distinguished with Deep Learning (Later)
A Xe ElectroLuminescence : AXEL
DBD18
21 Oct 2018

## Slide 7
9cm
φ10cm
~ 100kg scale
ton scale
Road map of the AXEL experiment
- Finish evaluation of the prototype detectors until 2020
- aiming to start physics run from 2021
2018 ~
2021 ~
202X ~
2014~2018
~φ50cm
~50cm
- ~0.08kg Xe
- Demonstrate the ELCC concept
- Energy resolution study
( 122keV, 356keV, 511keV )
- ~5.6kg Xe
- Know-how of enlargement
- Energy resolution study
(near the Q-value)
- Background study
- now, constructing
- Discovery(?)
- sweep out IH
- Physics run
- World record
A Xe ElectroLuminescence : AXEL
DBD18
21 Oct 2018

## Slide 8
AXEL experiments
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Future prospect
Summary
Contents
DBD18
21 Oct 2018

## Slide 9
Sensitive region : φ10cm × 9cm
# of channel : 64
Purpose : Demonstrate the performance of ELCC
9cm
φ10cm
5mm
Prototype detector
MPPCs
Sensitive to VUV light
PMTs
2.5cm
7.5mm
Prototype detector (1) : 10L prototype
DBD18
21 Oct 2018

## Slide 10
302keV
356keV
326keV
276keV
81keV
50keV
X-ray of Xenon
- Fitting by “ Σgaussian + ax+b” in low E region
- Fitting by “ Σgaussian + exp” in high E region
→ ⊿E : 2.54% FWHM at 356 keV
→ 0.97% FWHM at Q-value, extrapolated by √E
- Gas ： Xe 8 bar
- Edrift ：83 V/cm/bar
- EEL ：2.375 kV/cm/bar
- source : 133Ba
Evaluated a performance of the prototype detector
using 133Ba gamma-ray source (356keV)
Prototype detector (1) : 10L prototype
DBD18
21 Oct 2018

## Slide 11
Energy resolution at Q-value
- Estimated to 0.82 ~ 1.74 % FWHM at Q-value (2458keV)
- Simulation (Geant4) is also on-going to understand this result
Q-value
Target : 0.5% FWHM
A = 0.376 +/- 0.0186
B = 0.002 +/- 0.0008
-> Extrapolate to Q-value
FWHM 1.74% (@2458keV)
A = 0.406 +/- 0.0140
-> Extrapolate to Q-value
FWHM 0.82% (@2458keV)
Prototype detector (1) : 10L prototype
DBD18
21 Oct 2018

## Slide 12
AXEL experiments
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Future prospect
Summary
Contents
DBD18
21 Oct 2018

## Slide 13
unit
Electrode
PTFE
Insulator
- Evaluation of energy resolution near the Q-value
- Now, constructing……
- Field Shaper
- Discharge resistant : embedded electrode, insulator
- increase scintillation light yield due to PTFE reflection
- ELCC (readout structure of ionization signal)
- Prefabricated style → easily to extend
- Number of channels : ~1000 ch
- Design is almost fixed
- Cockcroft-walton
- Generate ~65kV
inside the vessel
- Low outgas (Polyimide)
DBD18
21 Oct 2018
~φ50cm
~50cm
Polyimide
FPC

## Slide 14
- Evaluation of energy resolution near the Q-value
- Now, constructing……
- Readout electronics
- Readout waveforms of MPPC : 56 ch/board
- Two Flash ADCs to achieve wide dynamic range : 1 p.e ~ 104p.e
- High Voltage supply to MPPCs (in the 0.2mV)
- Monitor MPPC gain constantly
→ adjust (feedback) gain in 0.25% accuracy
- Low cost
DBD18
21 Oct 2018

## Slide 15
AXEL experiments
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Future prospect
Summary
Contents
DBD18
21 Oct 2018

## Slide 16
- Gamma-ray with photoelectric absorption event will be a serious BG
- Topological information
- 0νββ decay has two blobs
- Photoelectric absorption of gamma event only has one blob
→ To Identify two blobs is very powerful strategy
0νββ
Gamma-ray
(simulation)
(simulation)
Future prospect
DBD18
21 Oct 2018

## Slide 17
Topological information
- Deep Learning(DL) is one of the options
- Learning with simulation of 0νββ and gamma-ray
- Pitch of readout cell is variable to optimization (performance vs costs…)
- Signal efficiency : 41% : BG : 121 evt/yr → 3.2 evt/yr w/ DL (1 ton Xe)
(assuming 10 tons of pressure vessel made of Oxygen-free Cu, 10mm-pitch readout)
- Estimated sensitivity : mββ = 32 meV (1 ton yr Xe, 10 mm-pitch)
Future prospect
DBD18
21 Oct 2018
signal
Gamma(BG)

## Slide 18
Future prospect
More ideas…
- Timing information of scintillation
- color represents the timing (ideal case)
0νββ Gamma
- in real case, it will be more complicated
due to
- depth of field
- time constant of scintillation etc…
- Thin, active vessel
- reduce 214Bi : thin
- detect α from 214Po : active
→ coincidence of Bi-Po
DBD18
21 Oct 2018

## Slide 19
AXEL experiments
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Future prospect
Summary
Contents
DBD18
21 Oct 2018

## Slide 20
AXEL is high pressure gas Xe TPC for 0νββ decay search
- Cellular readout structure (ELCC) is characteristic of AXEL
Small (10L) prototype detector has constructed
- Demonstrate the performance of ELCC
- ⊿ E : 0.82 ~ 1.74 %(FWHM, extrapolated to Q-value) is estimated
Large (180L) prototype detector is now constructing
- To demonstrate the performance of AXEL detector at near the Q-value
- To get the know-how to enlargement our detector
Aiming to mββ = 20 meV with some ideas
- e.g. Deep leaning, timing information, thin (active) vessel
Summary
DBD18
21 Oct 2018

## Slide 21
Thank you

## Slide 22
Backup
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 23
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018
T.Nakadaira
Shuhei Obara
Members

## Slide 24
Introduction : Neutrinoless Double Beta Decay (0νββ decay)
It occurs only if the neutrino has Majorana mass term
2νββ decay
0νββ decay
If the neutrino is Majorana ……
- naturally explains the smallness of the neutrino mass
- One of the conditions of Leptogenesis story
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 25
Introduction : Neutrinoless Double Beta Decay (0νββ decay)
Pioneering work by the NEXT experiment group demonstrated usability of high pressure xenon gas time projection chamber (TPC) for 0νββ decay search
Large target mass
Low BG
(BG rejection)
Energy
resolution
To discovery 0νββ decay ……
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 26
Contents
AXEL experiments
Simulation study
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Summary
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 27
Simulation study
square
1.0cm
1.0cm
2cm
0.5cm
0.58cm
0.6cm
Edrift=100V/cm/atm
Eanode=3kV/cm/atm
gmsh
elmer
hexagonal
Collection efficiency
of electric field line
is checked by simulation
(gmsh + Elmer)
our design
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 28
Line of electric field
Electric field strength along the line
(red : EL region)
Electron track by Garfield++
Generate EL lights by MC method
(reflect coefficient of PTFE : 60%)
Simulation study
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 29: Uniformity of EL generation
Simulation study
EL Yield is proportional to [electric field strength] x [path length]
Uniformity : 1.4%
Since initial electron number is 1e5, effect on energy resolution will be 1.4%/√1e5 = 0.005%
Electric field along the path
Initial position dependence of EL yield
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 30
Simulation study
Number of detected photons
Estimated energy resolution
Number of detected photons
Simulation process
  0nbb event by Geant4
  statistical fluctuation with fano factor
  drift to the ELCC plane with diffusion
  EL generation (6photon/e-)
Simulated energy resolution: 0.37%(FWHM)
  ionizing process: 0.27%
  EL process: 0.25%
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 31
Contents
AXEL experiments
Simulation study
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Summary
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 32
Gas system
- circulation pump : PumpWorks PW2070
- SEAS micro torr MC1-902FV
- API GETTER-I Re
Prototype detector (1) : 10L prototype
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 33
XeSAT2018 at Waseda University, 19 Sep 2018
81keV
51keV
30keV
302keV
356keV
326keV
276keV?
272keV?
- Fiducial cut
- Saturated event → cut
- Cell gain calibration
- MPPC saturation correction
etc……
- Gas ： Xe 8 bar
- Edrift ：83 V/cm/bar
- EEL ：2.375 kV/cm/bar
- source : 133Ba
Correction using 30 keV X-ray peak position
30keV
30keV
Details in the next page
Data and Analysis
Prototype detector (1) : 10L prototype

## Slide 34
MPPC saturation correction
- Signal is saturated as # of incident photons approaches the total number of pixel of MPPC
two time constants
Schematic of MPPC signal
Voltage
- saturation curve is determined by recovery
time of MPPC
- Measured recovery time of MPPC one by
one, and apply to analysis
Prototype detector (1) : 10L prototype
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 35
81keV
51keV
30keV
302keV
356keV
326keV
272keV?
- Fiducial cut
- Saturated events → cut
- Cell gain calibration
- MPPC saturation correction
etc……
- Gas ： Xe 8 bar
- Edrift ：83 V/cm/bar
- EEL ：2.375 kV/cm/bar
- source : 133Ba
Correction using 30 keV X-ray peak position
30keV
30keV
MPPC signal saturate as # of incident photons increases
- saturation curve is characterized by
MPPC recovery time
- measured recovery time one by one
→ apply to
correction
Data and Analysis
two time constants
Schematic of MPPC signal
Voltage
Prototype detector (1) : 10L prototype

## Slide 36
Fitting of the histogram
-
302keV
356keV
326keV
276keV
81keV
50keV
X-ray of Xenon
- Fitting by “ Σgaussian + ax+b” in low E region
- Fitting by “ Σgaussian + exp” in high E region
→ ⊿E : 2.54% FWHM at 356 keV
→ 0.97% FWHM at Q-value, extrapolated by √E
Prototype detector (1) : 10L prototype
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 37
Contents
AXEL experiments
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Future prospect
Summary
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 38
Prototype detector (2) : 180L prototype
- Evaluation of energy resolution near the Q-value
- Now, constructing……
Cockcroft-Walton for HV
Readout electronics
ELCC
Field cage
Pressure vessel
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 39
- Evaluation of energy resolution near the Q-value
- Now, constructing……
Cockcroft-Walton for HV
Readout electronics
ELCC
Field cage
Pressure vessel
Prototype detector (2) : 180L prototype
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 40
Pressure vessel
- SUS304L
- Volume : ~180L (Sensitive Volume : ~100L)
- Now, ready !
Prototype detector (2) : 180L prototype
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 41
- Evaluation of energy resolution near the Q-value
- Now, constructing……
Cockcroft-Walton for HV
Readout electronics
ELCC
Field cage
Pressure vessel
Prototype detector (2) : 180L prototype
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 42
ELCC
- Prefabricated style → easily to extend
- Number of channels : ~1000 ch
- Design is almost fixed
unit
Prototype detector (2) : 180L prototype
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 43
- Evaluation of energy resolution near the Q-value
- Now, constructing……
Cockcroft-Walton for HV
Readout electronics
ELCC
Field cage
Pressure vessel
Prototype detector (2) : 180L prototype
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 44
Field cage
- Alignment drift field by strip electrodes
- Reflecting scintillation photons by PTFE
- Withstand discharge structure
- Uniformity of Field strength is checked by FEM simulation
- Now, testing with 10L prototype detector
Electrode
PTFE
Insulator
Electric field simulation by FEM
Electric field
Prototype detector (2) : 180L prototype
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 45
- Evaluation of energy resolution near the Q-value
- Now, constructing……
Cockcroft-Walton for HV
Readout electronics
ELCC
Field cage
Pressure vessel
Prototype detector (2) : 180L prototype
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 46
Introduce low voltage into chamber and boost by Cockcroft-Wakton
inside the chamber to avoid discharge at feedthrough
- Low outgas due to Polyimide
- succeed to generate 10kV with a prototype
Input amplitude : 540 V
Prototype detector (2) : 180L prototype
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 47
- Evaluation of energy resolution near the Q-value
- Now, constructing……
Cockcroft-Walton for HV
Readout electronics
ELCC
Field cage
Pressure vessel
Prototype detector (2) : 180L prototype
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 48
Readout Electronics
- Readout waveforms of MPPC : 56 ch/board
- Two Flash ADCs to achieve wide dynamic range : 1 p.e ~ 104p.e
- High Voltage supply to MPPCs (in the 0.2mV)
- Monitor MPPC gain constantly
→ adjust (feedback) gain in 0.25% accuracy
- Low cost
Prototype detector (2) : 180L prototype
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 49
Readout Electronics
- Succeed to readout waveform signals with both of ADCs
Prototype detector (2) : 180L prototype
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 50
AXEL experiments
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Future prospect
Summary
Contents
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 51
Future prospect
Sensitivity estimation for 1 ton detector
- Need to reach mββ = 20 meV
- Background free is required
- 214Bi (2447 keV) is serious BG source
- Main source : Pressure vessel (~10 ton)
- Even if we use oxygen-free copper
2.9 ppt 214Bi (cf. EXO-200)
→ 75 event/year for 1 ton detector
arXiv.1502.00581
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018

## Slide 52
Topological information
- Deep Learning is one of the options
- Learning with simulation of 0νββ and gamma-ray
- Pitch of readout cell is variable to optimization (performance vs costs…)
- Signal efficiency : 41% : BG : 121 evt/yr → 3.2 evt/yr (1 ton Xe)
(assuming 10 tons of pressure vessel made of Oxygen-free Cu, 10mm-pitch readout)
- Estimated sensitivity : mββ = 32 meV (1 ton yr Xe, 10 mm-pitch)
Future prospect
DBD18
21 Oct 2018
signal
Gamma(BG)
model1_02

## Slide 53
Future prospect
Further more…
- Pressurized water shield
- water Cherenkov can be used for muon veto
- thin pressure vessel to reduce mass → reduce 214Bi BG
- Active shield vessel
- detects alpha and beta ray event of 214Bi in the materials of vessel
Polyethylene Naphthalate
DBD18 at Hilton Waikoloa village, Hawaii, 21 Oct 2018