## Slide 1: High pressure xenon gas detector with segmented electroluminescence readout for 0nbb search
Kiseki Nakamura | Kobe university
for the AXEL collaboration

## Slide 2: AXEL member in Kyoto
Atsuko K. Ichikawa
Tsuyoshi Nakaya
Kiseki Nakamura
Sei Ban
Masashi Yoshida
Kazuhiro Nakamura
Shunsuke Tanaka
(speaker)

## Slide 3: AXEL experiment
High pressure xenon gas TPC for 0nbb search
field cage
PMT
136Xe 10atm
~-200kV
ELCC
e-
scintillation
photon
~4m
Background rejection: tracking by segmented EL readout
Large mass: high pressure
~ ton scale
Energy resolution: gaseous xenon + electroluminescence (EL) readout
target: 0.5%FWHM
SiPM
EL
~-15kV
0V

## Slide 4: AXEL experiment
High pressure xenon gas TPC for 0nbb search
field cage
PMT
136Xe 10atm
~-200kV
ELCC
e-
scintillation
photon
~4m
Background rejection: tracking by segmented EL readout
Large mass: high pressure
~ ton scale
Energy resolution: gaseous xenon + electroluminescence (EL) readout
target: 0.5%FWHM
SiPM
EL
~-15kV
0V
Similar concept as NEXT experiment
We introduce a new idea "ELCC" for signal readout
Need proof-of-principle by simulation and prototype detectors

## Slide 5: Segmented EL readout: ELCC
Detect EL photons for cell by cell
Energy measurement and tracking
Good uniformity in wide area
Rigid structure --> large size
SiPM
EL

## Slide 6: ELCC simulation
Electric field simulation (gmsh + elmer)
By applying high electric field in the EL region, electric field lines are pulled into the cell hole
1.0cm
1.0cm
2cm
0.5cm
0.58cm
0.6cm
Edrift=100V/cm/atm
Eanode=3kV/cm/atm
gmsh
elmer

## Slide 7: Collection of line of electric field
Larger aperture is better
Taking some Edrift, large EEL is better (Edrift=100V/cm/atm, EEL>2.5kV/cm/atm)
square
cell pitch
hole radius
EL length
Edrift
EEL

## Slide 8: Collection of line of electric field
Hexagonal placement is better
Next prototype will be OK
square
cell pitch
hole radius
EL length
Edrift
EEL
hexagonal
next prototype
current prototype

## Slide 9: Uniformity of EL generation
EL Yield is proportional to [electric field strength] x [path length]
Uniformity : 1.4%
Since initial electron number is 1e5, effect on energy resolution will be 1.4%/√1e5 = 0.005%
Electric field along the path
Initial position dependence of EL yield

## Slide 10: Electron and photon propagation simulation
Electron track by Garfield++
EL photons by Monte Carlo method
6photon/e- @SiPM(3mm square)
1000ev
1000ev
hit timing
detected photon num
hit position at SiPM
1000ev

## Slide 11: Estimation of energy resolution
Simulation process
  0nbb event by Geant4
  statistical fluctuation with fano factor
  drift to the ELCC plane with diffusion
  EL generation (6photon/e-)
Simulated energy resolution: 0.37%(FWHM)
  ionizing process: 0.27%
  EL process: 0.25%
Detected EL num
Detected EL num

## Slide 12: Prototype detector
Parameters
  Sensitive region: 6 x 6 x 9 cm
  Cell num: 64
  Gas pressure: 4 bar
  Edrift: 100 V/cm/atm
  EEL: 2.7kV/cm/atm
MPPC-VUV3
  PDE: 23%
  Size: 3 x 3 mm2
Prototype detector
anode electrode
MPPCs
7.5mm
9cm
arxiv: 1701.03931

## Slide 13: ELCC design
cross section view
To prevent discharge, PTFE holes is slightly smaller than anode(Cu) holes

## Slide 14: High voltage applying
Two HV modules to control both EL field and drift field
  HFR10-30N, HFR10-20N [Matsusada-precision]
Diode and resistance for circuit protection
SiPM
EL
-15kV
-24kV

## Slide 15: Gas circulation system
Circulate high pressure xenon gas
  pump: PumpWorks PW2070
  SAES micro torr MC1-902FV
  API-GETTER-I -Re
  Number of photons slightly increase at first
used for analysis

## Slide 16: Event sample
Waveforms of MPPC and PMT
EL light & scintillation light are observed
MPPC: 65MHz 12bit 2Vpp
PMT: 100MHz 14bit 2Vpp

## Slide 17: Analysis flow
Fiducial cut
  XY by hit channel, Z by PMT timing
EL gain correction
  Measure each cell gain by 30keV peak
Dark count correction
  Depend on time duration of EL photon
fiducial
dark
EL-gain

## Slide 18: Measured energy spectrum
Four (five?) peaks are observed using 57Co source
X-ray (Ka)
29.78 keV
X-ray (Kb)
33.62 keV
Escape peak (Kb) ?
88.44 keV
Full peak
122.06 keV
Escape peak (Ka)
92.28 keV

## Slide 19: Measured energy resolution
Measured energy: 30,34,88,92,122 keV
Extrapolating 2.5MeV by assuming
  : 1.61%FWHM
  : 0.59%FWHM
0.5%FWHM@2.5MeV

## Slide 20: Upgrade of ELCC structure
New ELCC will come soon for testing...
  Higher energy measurement (511keV gamma-ray)
  Multi electrode (scale up study)
  Hexagonal placement (better than square one)
old
new
1/3 of anode hole plate
GND mesh

## Slide 21: Large prototype project
100L scale detector
Purpose
  test at 2.5MeV
  test tracking
  get large size technique
Status
  Chamber will come by this summer
  Electronics development ongoing
  Developing Cockcroft-Walton high voltage generation
  Cabling test

## Slide 22: Simulation study for BG rejection
Track topology (by Geant4)
  2-blobs : 0nbb
  small : a-ray BG
  multi-site : g-ray BG with Compton scattering (~98%)
Basically, 2.5MeV g-ray with photo absorption (~2%) is the serious background
0nbb
a-ray (2.5MeV)
g-ray (2.5MeV)

## Slide 23: BG simulation with Geant4
Assumption
  1 ton 136Xe
  2.9ppt 214Bi in chamber
Sensitivity
  mbb=60meV (current)
  mbb=20meV (reduce chamber mass: 10ton --> 100kg)
current simulation
chamber mass: 10ton --> 100kg
original electron track
reconstructed track
energy of lower blob
Upper limit of EXO's copper
Heaviest component

## Slide 24: Summary
AXEL project developing high pressure xenon gas TPC for 0nbb search.
Segmented electroluminescence readout (ELCC) is key component.
Simulated performance of ELCC is good.
Energy resolution measured by current prototype detector: 0.6-1.6%FWHM @ 2.5MeV
Large prototype construction started.
1ton detector sensitivity will reach ~20meV

## Slide 25: High energy resolution
Ionization process
  Use gaseous xenon
  W-value = 22.1eV
  Fano-factor = 0.13
  => 0.25%(FWHM) @2.5MeV
Signal multiplication
  Use ElectroLuminescence (EL)
  light yield/length is proportional to the electric field
  amplification fluctuation is small
NIMA396(1997)360
Energy reolution %
0
2
4
6
8
0
density [g/cm3]
1
2
3
4
100atm
Eγ=662keV
ElectroLuminescence
Avalanche
Noble gas detector

## Slide 26: New GND mesh idea
Fine etched electrode
  Isolate cell from EL photon
  Strong for stretching and deflection
PTFE
MPPC
MPPC

## Slide 27: Tracking
rate of g-ray from
214Bi (2448keV)
chamber mass
107[g](=10ton)
contamination
2.9x10-12(=2.9ppt)
Avogadro number
6.02x1023[/mol]
half life of 238U
4.468x109[year]
atomic weight of 238U
238 [g/mol]
branching ratio
0.0157
180000
[cts/year]
process | 0nbb efficiency | g (2448keV) rate
initial condition | 100% | 180000 cts/year
fiducial-cut | 79% | 12000 cts/year
multi-cluster-cut | 49% | 75 cts/year
2-blob-selection | 19% | 5.5 cts/year
solid angle
(chamber --> gas)
98% is Compton
Simulated signal-efficiency and BG-rate
for each analysis steps