## Slide 1
A Xenon ElectroLuminescence detector
for 0ν2β search
S.Obara
for the AXEL collaboration
2018/09/06
Symposium for Muon & Neutrino Physics 2018

## Slide 2: Neutrinoless double-beta decay
n
n
e-
e-
2ν2β mode
n
n
e-
e-
×
0ν2β mode
136Xe
136Ba
136Cs
× Beta decay
○ Double beta-decay
Rare decay (T>1026yr)
Emits two electrons
A proof of Majorana neutrino
Limits on absolute ν-mass
2ν2β
0ν2β
Qββ=2.46MeV

## Slide 3: What are important for 0ν2β
Ann.Rev.Nucl.Part.Sci.52:115-151,2002
Considering the event-rate within the ROI …
Suppressing radioactive impurities
High energy resolution
Large mass
Realize
Background-free search
with
Phys. Rev. Lett. 117, 082503 (2016)
; background limited case
; background free case
← Kai’s slide showed same formula but for half-life; 1/T ∝ m2

## Slide 4: We need more exposure
1 ton × 10yr
100 ton × 10yr
BG-limited case
we have to prepare 100ton targets
If BG-Free,
1 ton × 10yr
thanks to m∝1/√MT, we can reach NH with 1-ton detector
~500kg-yr
Background-free & ton-scale detector
We really need

## Slide 5: Keys for BG-free search …
High energy resolution
Low radioactive contamination
Background identification
depends on ΔE
Suppress the BG with
in the ROI

## Slide 6: Keys for BG-free search …
High energy resolution
Low radioactive contamination
Background identification
depends on ΔE
Suppress the BG with
in the ROI
Using Electroluminescence
Using Event topology
High Pressure Gas TPC; AXEL
+ Scalability

## Slide 7: High-ΔE for Electroluminescence
Xe
Xe
Xe
e
E
EL photon
EL process
Linear amplification ⇔ Less fluctuation in energy
ElectroLuminescence process
Fano-factor; 0.13
W-value; 22.1 eV ⇒ target ΔE ~ 0.5% (FWHM @ Qββ=2.46MeV)
Small Ionization of Xenon-gas
→
NEXT and AXEL use

## Slide 8: AXEL - Conceptual Design -
VUV PMTs for T0 signal
Cockcroft-Walton Voltage multiplier for HV supply
ELCC for energy & tracking
Drift Field Cage
E
Drift Electron
Scintillation
136Xe for 0ν2β
1ton xenon gas
10 bar
like NEXT, PANDAX-III

## Slide 9: Characteristic of AXEL
ref; JHEP 1605 (2016) 159
NEXT
Energy read-out by PMTs
Tracking read-out by SiPMTs
Mesh structure for anode
AXEL
Energy & Tracking read-out by ELCC
Rigid structure of ELCC; for scalability
NIM, A 875 (2017) 185-192

## Slide 10: ELCC
(Electroluminescence Light Collection Cell)
Anode Cu plate
PTFE insulator
Mesh electrode
MPPC array
~100 V/cm/bar
~2.5 kV/cm/bar
EL process area
Drift area
Fix EL process area in a cell → Uniform EL gain wherever the initial electron is
Rigid structure → We can scale up to the large-size detector, starting with small prototype

## Slide 11: Prototype detectors
2015
2018
10L - size
Check ΔE
Proof concepts
180L - size
Proof ΔE @ Q-value
Check ambient radioactivities & backgrounds
Now constructing …
202?
3000L - size
@ underground
Physics search
20??
Large - size
L 9 cm
Φ 10 cm
(10g xenon)
(8.6kg xenon)
L 83 cm
Φ 55 cm
(100 kg xenon)

## Slide 12: 10L-prototype ΔE
L 9 cm
Φ 10 cm
30 keV
81 keV
51 keV
276 keV
302 keV
326 keV
356 keV
Target: 0.5% FWHM
Extrapolate to Q-value
1.74% FWHM w/
0.82% FWHM w/
Check ΔE with 57Co, 133Ba
Q-value (2.46 MeV) is too large for this small size
Estimated to 0.8~1.8% FWHM @ Q-value
worse ΔE than expectation
Q-val.

## Slide 13: 180L prototype detector
Chamber
ELCC
Field cage
Electronics
Now constructing …

## Slide 14: 180L prototype detector
Chamber
ELCC
Field cage
Electronics
L83cm
Φ55cm
Test ΔE @ Q-value (2.5 MeV)
~ 100L FV
~ 1000ch MPPCs
SUS
(underground)
×10 volume than current

## Slide 15: 180L prototype detector
Chamber
ELCC
Field cage
Electronics
Sectional view of ELCC design
Cell Φ 6mm
Unit
ELCC

## Slide 16: 180L prototype detector
Chamber
ELCC
Field cage
Electronics
Prototype
Cockcroft-Walton
PTFE field cage
For HV supply
Currently feasibility check with HP10L
Alignment of Electric field
Reflection of scintillation light
check with HP10L

## Slide 17: 180L prototype detector
Chamber
ELCC
Field cage
Electronics
Test a prototype board
HV supply for MPPCs (in the 0.2 mV)
Two ADCs of dynamic range; 1 p.e. ~105 p.e.
A few hundred μsec wide for waveform

## Slide 18: Prototype detectors
2015
2018
10L - size
Check ΔE
Proof concepts
180L - size
Proof ΔE @ Q-value
Check ambient radioactivities & backgrounds
Now constructing …
202?
3000L - size
@ underground
Physics search
20??
Large - size
L 9 cm
Φ 10 cm
(10g xenon)
(8.6kg xenon)
L 83 cm
Φ 55 cm
(100 kg xenon)

## Slide 19: Radioactivities
Main source
Chamber vessel
Even if we use an oxygen-free copper,
2.9 ppt 214Bi (cf; EXO-200 ) ⇔ 75 evt/yr for 1ton-detector
Vessel is the largest mass ~ 10ton
arXiv:1106.3630v1 [physics.ins-det] from NEXT paper
2614 keV
2382 keV
2447 keV
2458 keV
Even if we achieve ΔE ~ 0.5% FWHM,
214Bi γ-ray 2447keV
is background for 2458 keV of 0ν2β

## Slide 20: Topology identification
0ν2β (double-β)
214Bi (gamma-ray)
Identify the two blobs
0ν2β has two blobs
Photoelectric absorption of 214Bi-gamma has one blob
*
* A point with large energy deposit soon before the stop

## Slide 21: Furthermore …
Deep Learning
Challenge
214Bi
0ν2β
Th.
sig. eff. ; 42%
BG rate; 75 → 7.9 [evt/yr]
A prototype machine learning
(assuming the 1ton AXEL detector)
TPC has a topology
Recent libraries are developed & useful for “image identification”
It has a potential
signal like
background like

## Slide 22: The outer detector plans
like as underground detectors; Super-K, SNO…
Pressurized water
for 1ton-detector
Water Cerenkov
is used for cosmic muon veto
Pressurized water
makes thin inner-vessel
⇔ reduce mass
⇔ suppress BG
Active shield vessel
detects ambient backgrounds from vessel
Polyethylene Naphthalate

## Slide 23: Summary
0ν2β search needs BG-free and 1ton-scale detector
AXEL is a high-pressure Xe gas TPC with an unique readout sys. ELCC
10L prototype
  checked ΔE in lower energy range
  0.8~1.8% FWHM @ Q-value (extrapolate)
180L prototype
  now constructing
  will check ΔE @ Q-value
  final test before placing at underground

## Slide 24: backup

## Slide 25: High-ΔE for Electroluminescence
Xe
Xe
Xe
e
E
EL photon
EL process
ファノファクター, W-valueの説明
Linear amplification ⇔ Less fluctuation
Electroluminescence process
Fano-factor; 0.13
W-value; 22.1 eV ⇔ ΔE ~ 0.3% @ Qββ=2.46MeV
Small Ionization of Xenon-gas

## Slide 33
136Xe
136Ba
136Cs
× Beta decay
○ Double beta-decay

## Slide 34: What important is for 0ν2β
Ann.Rev.Nucl.Part.Sci.52:115-151,2002
Considering the event-rate within the ROI …
Suppress radioactive impurities
High energy resolution
Large mass
Realize
Background-free search
with
Phys. Rev. Lett. 117, 082503 (2016)
Notes: 61-165meV

## Slide 35: 122keV-gamma from 57Co
NIM, A 875 (2017) 185-192

## Slide 36
ELCC unit/仕様書 for review
2018年8月6日
ELCCユニットの断面の概念図
HP180L
PTFE
Unit-2
PTFE
Unit-1
PEEK
PEEK
Frame
For z pos. of unit
For z pos. (inside unit)
Pin for xy position
Screw for fixed to frame
(M3, L20)
Screw for PTFE - MPPC board
(M2.6)
Electrode at unit connection part
Dielectric sheet
(for corona discharge)
MPPC
MPPC
MPPC