## Slide 1: High-pressure Xe gas TPC for BG-free 0v2b search
S.Obara,
For the AXEL Collaboration
Neutrino-less Double Beta-Decay (0v2b)
ELCC
Large Volume, Good Energy Resolution, Tracking
keywords

## Slide 2: Outline
Phys. Motivation ; Neutrinoless DBD (0v2b)
AXEL-Detector
    Conceptual Design Overview
    Unique Read-out System ; ELCC
    Challenges
    Future Prospects & Current Status
Summary

## Slide 3: Phys. Motivation; 0v2b
0v2b is allowed
the See-saw mechanism  light mv
the RH heavy-neutrino  matter dominant
Phys. Rev. Lett. 117, 082503 (2016)
Search two-electrons emission
Limits on T1/2 <=> Eff. Mass
<mββ>2 = |ΣUmi|2
LIMIT SCHEME
IN MAJORANA CASE (v=vC),

## Slide 4: What keys for 0v2b observation
Large Mass
BG-Free Technique
Good Energy Resolution
KamLAND-Zen used 400 kg of 136Xe
Liq. Scintillator detector is useful

## Slide 5: What keys for 0v2b observation
Large Mass
BG-Free Technique
Good Energy Resolution
GERDA, CUORE has good ΔE ~ 0.2%
2v2b spectrum is unavoidable BG
Germanium detector is useful

## Slide 6: What keys for 0v2b observation
Large Mass
BG-Free Technique
Good Energy Resolution
In order to test the normal hierarchy, we need
  100 ton ×10 yr for BG-limited
  1 ton ×10 yr for BG-free
SENSITIVITY
; for BG-limited case
; for BG-free case

## Slide 7: High-Pressure Xenon Gas TPC
Xenon Gas
  Small W-value
  Electroluminescence process
Large Mass
BG-Free Technique
Good Energy Resolution
High-Pressure Gas
  90% enrich 136Xe
Tracking
  Identify two-electrons
⇒ AXEL

## Slide 8: AXEL – Conceptual Design -
A Xenon ElectroLuminescence
Tracking Plane
T0 Timing
Drift Field Cage
Pure Xenon Gas TPC
136Xe = 0v2b nuclei
Long life of 2v2b mode
Easy to enrich
Easy to distillation
Chemical stable
Scintillation W=21eV
× Easy to discharge

## Slide 9: AXEL – Conceptual Design -
A Xenon ElectroLuminescence
Tracking Plane
T0 Timing
Drift Field Cage
Scintillation & PMTs
λXe ~ 178 nm
Use VUV-sensitive & 1MPa tolerable PMTs by Hamamatsu Photonics K.K.
Obtain T0 of 0v2b signal
 Used to reconstruct Z position from ionization signal
scintillation

## Slide 10: AXEL – Conceptual Design -
A Xenon ElectroLuminescence
Tracking Plane
T0 Timing
Drift Field Cage
Use ElectroLuminescence Process
for the ionization electrons tracking
Linear Amplification
Good Energy Resolution
cf1; NEXT also uses EL-process but with mesh plane
cf2; PANDAX-III uses MM for tracking readout

## Slide 11: ELCC (Electroluminescence Light Collection Cell)
Cell-Type Tracking Plane
e-
EDrift
MPPC
MPPC
MPPC
EEL
e-
e-
e-
e-
~0.1kV/cm/bar
~2.5kV/cm/bar
Collect the drift electrons into cells
Linear Amp. via EL-process
Detect EL-photons by MPPCs
10mm-pitch
EL area
Drift area

## Slide 12: ELCC -Pitch Optimization-
1.0cm
1.0cm
2cm
0.5cm
0.58cm
0.6cm
Edrift=100V/cm/atm
Eanode=3kV/cm/atm
gmsh
elmer
Optimize Parameter; hole-size, hole-pitch
Max; Electron collection efficiency with ΔE
Use; Finite Element Method
Gmsh, ElmerSolver, and Garfield++
=> Φ5.5mm, 10mm-pitch

## Slide 13: Challenges
Discharge in Pure Xenon Gas TPC
    Easy to discharge
    Admixture makes worse ΔE
Non-Linearity of MPPC
    Estimate correction factor with calibration
Tracking Identification with Deep Learning
    214Bi γ-ray (2,447keV) & 0v2b signal (2,458keV)
Positive-Ion Detection
    Ionized Xe+ is also able to observe (?)
Active-shield Outer Detector
    Liq.-Scintillator ? Water ? Pressurized ?

## Slide 14: Challenges – Discharge Prob. -
× Admixture-gas
 useful for discharge problem
 but makes worse ΔE
◯ Block Electric Path
 Fill with insulator b/w electrode & chamber-wall
◯ Slowly Drift-HV suppling
Dominant discharge comes from the drift HV supplier electrodes
Ring-Electrode
PTFE-Ring
Insulator
Pure Xenon
= Easy to discharge !!

## Slide 15: Challenges – Deep Learning -
arXiv:1106.3630v1 [physics.ins-det] from NEXT paper
0v2b signal (MC)
214Bi background (MC)
MC
Dominant BG => 214Bi from vessel
cannot be identified with only ΔE
but we can use also topology !!
Current Deep Learning identification will reach mbb=32meV with 1ton・year
Topology Identification

## Slide 16: Challenges – Xe+ Track -
Support
Tracking Identification
Ionized xenon ions also drifts to opposite side
It’s just feasibility study but…
If we can use Xe+ tracking additional to usual e-, the tracking identification will be improved !!
Very preliminary
DAQ with Oscilloscope
[msec]
0 20 40
[V]
Sci. for 241Am-α
Xe+ induced electrons ?
241Am as α-ray source
PMT
5.4MeV-α
scintillation
Wire; -1500V
E
・
e- induced
・
Drift Xe+
1atm Xe

## Slide 17: Challenges – Active Shield -
PolyethyleneNapthalate Vessel
In order to shield from ambient radioactivity, an Active Shield is useful
Water ?, Water+Gd ?, Liquid Scintillator ?
Pressurized water makes thinner-chamber
Can the scintillator vessel be used for the chamber ?
Underground Detector

## Slide 18: Current Status - HP10L -
7.5mm
9cm
φ10cm
5mm
2cm
VUV-PMT
MPPC array
AXEL HP10L prototype

## Slide 19: Current Status - HP10L -
L 9cm
φ10cm
Test our conceptual design with Very small detector (Xe~80g)
2,458 keV; Q-value of 0v2b
We have only low-energy data
But with extrapolation,
ΔE = 0.8~1.7% FWHM @ 2,458 keV
Extrapolation Function
302keV
356keV
326keV
276keV
with 133Ba

## Slide 20: Future Prospects
2014-2018
2019~
2021~
20XX~
L 9cm
φ10cm
100kg-scale detector
@ Underground
1ton-scale detector
Physics search
Fin. R&D with small detector
Now constructing 6kg-scale detector (HP180L)
Checking detail of ΔE @ Q-value
Background study
Know-how of enlargement

## Slide 21: HP180L prototype
Φ 55 cm
L 83 cm
SUS304
56×27 = 1,512 MPPCs (Hamamatsu) on
Unit-divided ELCC tracking plane with each 56 ch
Readout & Bias-HV supply via long FPC cable
Dynamic range FADC; 1~104p.e.
Also HV supply
10 VUT-PMTs &
LED for calibration
HV-Feedthrough
w/ LEMO connector
Input AC-HV
Generate DC-HV with
Cockcroft-Walton circuit

## Slide 22: Unit-ELCC
Φ ~55cm
7×8cm
A Unit
56 holes
Φ5.5mm hole

## Slide 23: Electronics board for HP180L
Waveform read-out from MPPCs; 56ch/board
Dynamics range of Flash ADC; 1p.e.~104p.e.
Monitor & Adjust the gain with feedback
HV supply to each MPPC (in the 0.2mV)

## Slide 24: Cockcroft-Walton Circuit for Drift Electric Field Supply
Input amplitude : 540 V
Not to discharge at the feedthrough
HV for the Drift-Electric-Field is generated in the TPC
※ prototype

## Slide 25: Summary
“AXEL” is a high-pressure pure xenon-gas TPC for 0v2b search;
    Good ΔE ~ 0.5% FWHM @ 2,458keV
    Large Target Mass ~ 1ton
    Background-free technique
“ELCC” is our unique readout-sys. using Electroluminescence-process & cell-type tracking plane
Fin. R&D of the conceptual design with small prototype (2014-2018)
Now constructing next prototype
(I hope) in the near future, find 0v2b signal

## Slide 26: BACKUP

## Slide 27: One of the future AXEL

## Slide 28: MPPC gain correction
Determine saturation-curve by recovery-time of MPPC
Measure recovery-time of MPPC one by one, and Apply to analysis
Voltage
Waveform Image of MPPC
Time Constants

## Slide 29: Deep Learning
signal
background
Sig. Eff = 40.04%
BG rate 101.9 evt/yr → 0.35 evt/yr
Assuming 10 tons of Oxygen-free Cu-vessel
T1/2 > 1.01e+27 yr (mbb < 19.73 – 53.46 meV)
Model07_01_11
Based on CNN, DenseNet
GeForce GTX 1080Ti 11GB
DDR4-2400 8GB×4
Core i7-7800X
Other HPXeTPCs are also trying

## Slide 30: Current Status - HP10L -
302keV
356keV
326keV
276keV
81keV
50keV
X-ray of Xenon
Gas; Xe 8 bar
Edrift; 83 V/cm/bar
EEL; 2.375kV/cm/bar
Source; 133Ba
ΔE = 2.54% FWHM @ 356 keV
 ΔE = 0.97% FWHM @ 2,458 keV

## Slide 31: AXEL – Conceptual Design -
A Xenon ElectroLuminescence
@ Kamioka Underground Lab.
1ton High-pressure 136Xe gas
Unique Readout-sys. ELCC
Tracking with Deep Learning
Positive-Ion tracking

## Slide 32
2,458 keV; Q-value of 0v2b
302keV
356keV
326keV
276keV
Energy [keV]
Energy Resolution (FWHM) [keV]
Number of Observed Photons
Extrapolation Function