## Slide 1: High pressure Xe gas TPC for neutrinoless double-beta decay search
Sei Ban
Kyoto University
For the AXEL collaboration
TAUP2019 at Toyama 12 Sep 2019

## Slide 2
AXEL experiment
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Future prospect
Summary
Contents
TAUP2019
12 Sep 2019

## Slide 3
AXEL experiment
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Future prospect
Summary
Contents
TAUP2019
12 Sep 2019

## Slide 4
High pressure Xe gas TPC with unique cell readout structure
for 0νββ decay search
136Xe 6~10 bar
ELCC plane
150~200kV
PMT
e
Atom
photon
Linear response to applied electric field
Without avalanche process
→ less fluctuation of multiplication
Detail is in the next page
  ● Electroluminescence (EL) process
Detection of Ionization signals
→ ton scale 136Xe(ββ-decay nucleus) gas
→ goal : 0.5%FWHM @ Q-value
Φa few meters
a few meters
Scintillation
Ionization
electrons
Good energy resolution
Tracking
(BG rejection)
A Xe ElectroLuminescence : AXEL
TAUP2019
12 Sep 2019
Large mass

## Slide 5
Electroluminescence Light Collection Cell : ELCC
- Energy measurement and Tracking
- Uniform response regardless of event position
- Extendable to large size thanks to its rigid structures
EDrift
MPPC
MPPC
MPPC
EEL
e-
e-
e-
e-
Ionization electrons are collected into cells
if EEL > EDrift , And generate EL light
Simulation study of ELCC was done and presented
in XeSAT2017
( https://indico.cern.ch/event/573069/sessions/230066/attachments/1440275/2217034/kisekinakamura_20170405_XeSAT.pdf )
A Xe ElectroLuminescence : AXEL
TAUP2019
12 Sep 2019

## Slide 6
expected event displays
(simulation : 10 bar Xe, 15mm-pitch, 1MHz sampling)
0nbb
a-ray (2.5MeV)
Compton g-ray (2.5MeV)
simulation
Event topology from hit pattern and waveform
- α-ray and γ-ray multi-site events are firmly
removed
- γ-ray photo-absorption events are
distinguished with Deep Learning (next page)
A Xe ElectroLuminescence : AXEL
TAUP2019
12 Sep 2019

## Slide 7
- Gamma-ray photo-absorption event will be a serious BG : mainly from 214Bi
- Topological information
- 0νββ decay has two blobs
- Photoelectric absorption of gamma event has only one blob
0νββ
Gamma-ray
(simulation)
(simulation)
TAUP2019
12 Sep 2019
A Xe ElectroLuminescence : AXEL

## Slide 8
Deep Learning
- Distinguish signals (0νββ) from BGs (gamma) using topological information
- Learning with simulated 0νββ and gamma-ray
- Signal efficiency : 50%, BG rejection : 99.95% by Deep learning)
- Estimated sensitivity : T0ν1/2 = 1.0×1027 year, BG : 0.8 cnt/yr (1 ton Xe, 6 years)
(assuming 10 tons of pressure vessel made of Oxygen-free Cu, 10mm-pitch readout)
TAUP2019
12 Sep 2019
A Xe ElectroLuminescence : AXEL

## Slide 9
9cm
φ10cm
~ 100kg scale
ton scale
Road map of the AXEL experiment
- Finish evaluation of the prototype detectors until 2021
- aiming to start physics run from 2022
2018 ~
2022 ~
202X ~
2014~2018
~φ50cm
~50cm
- ~0.08kg Xe
- Demonstrate the ELCC concept
- Energy resolution study
( 122keV, 356keV)
- ~5.6kg Xe
- Know-how of enlargement
- Energy resolution study
(511 keV ~ near the Q-value)
- Background study
- now, commissioning
- Discovery(?)
- sweep out IH
- Physics run
- World record
A Xe ElectroLuminescence : AXEL
TAUP2019
12 Sep 2019

## Slide 10
AXEL experiment
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Future prospect
Summary
Contents
TAUP2019
12 Sep 2019

## Slide 11
Sensitive region : φ9cm × 9cm
# of channel : 64
Purpose : Demonstrate the performance of ELCC
9cm
φ9cm
5mm
Prototype detector
Sensitive to VUV light
2.5cm
7.5mm
Prototype detector (1) : 10L prototype
TAUP2019
12 Sep 2019
MPPCs
PMTs

## Slide 12
302keV
356keV
326keV
276keV
81keV
50keV
X-ray of Xenon
- Fitting by “ Σgaussian + ax+b” in low E region
- Fitting by “ Σgaussian + exp()” in high E region
→ ⊿E : 2.54% FWHM at 356 keV
→ 0.97% FWHM at Q-value, extrapolated by √E
- Gas ： Xe 8 bar
- Edrift ：83 V/cm/bar
- EEL ：2.375 kV/cm/bar
- source : 133Ba
Evaluated a performance of the prototype detector
using 133Ba gamma-ray source (356 keV)
Prototype detector (1) : 10L prototype
TAUP2019
12 Sep 2019

## Slide 13
Energy resolution at Q-value
- Evaluation with two assumption : FWHM = or
- Estimated to 0.82 ~ 1.74 % FWHM at Q-value (2458 keV)
Q-value
Target : 0.5% FWHM
A = 0.376 +/- 0.0186
B = 0.002 +/- 0.0008
-> Extrapolate to Q-value
FWHM 1.74% (@2458keV)
A = 0.406 +/- 0.0140
-> Extrapolate to Q-value
FWHM 0.82% (@2458keV)
Prototype detector (1) : 10L prototype
TAUP2019
12 Sep 2019

## Slide 14
AXEL experiment
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Future prospect
Summary
Contents
TAUP2019
12 Sep 2019

## Slide 15
Components
~50cm
TAUP2019
12 Sep 2019
Prototype detector (2) : 180L prototype
Electrode
PTFE
Insulator
- Field Shaper
- Discharge resistant : embedded electrode, insulator
- increase scintillation light yield by PTFE reflection
- ELCC
- Prefabricated style → easily to extend
- Number of channels : ~1000 ch
- Cockcroft-walton
- Generate ~65kV
inside the vessel
- Low outgas (Polyimide)
~φ50cm
~50cm
Prototype
- Readout electronics
- waveforms of MPPC : 56 ch/board
- Bias Voltage supply to MPPCs (in the 0.2mV)
Adjustable for each channel
: 1 p.e ~ 104p.e
- FPC
- Signal, Bias line for MPPCs
- Feedthrough
Polyimide
FPC
unit

## Slide 16
Commissioning with a single unit
- evaluation is done using 30 keV peak
- The outer most layer is used as veto region
TAUP2019
12 Sep 2019
Prototype detector (2) : 180L prototype
- Gas ： Xe 2.3 bar
- Edrift ： 100 V/cm/bar
- EEL ： 3.0 kV/cm/bar
- DAQ time :
Dummy unit
Dummy unit
Red : veto
dead

## Slide 17
EL gain calibration
- EL gain of each cell differs due to (for example)
- Photon detection efficiency of MPPCs
- Processing errors of structures
- Cell gain calibration is performed using peak position of 30 keV
- Gain uniformity improves ( σ : 3.29% → 0.21% )
TAUP2019
12 Sep 2019
Prototype detector (2) : 180L prototype
- Gas ： Xe 2.3 bar
- Edrift ： 100 V/cm/bar
- EEL ： 3.0 kV/cm/bar
- DAQ time :
Peak position [photons]
Peak position [photons]
Distribution of peak position
Distribution of peak position

## Slide 18
TAUP2019
12 Sep 2019
Prototype detector (2) : 180L prototype
MPPC saturation correction
- Signal is saturated as # of incident photons approaches the total
number of pixel of MPPC
- Saturation curve of each MPPC is measured,
and correction is applied to analysis
Nobserved
Nref
Response function is
described as follow
Nobs : detected #photons
Nref : expected #photons
Npix : #pixel of MPPC
τ : recovery time

## Slide 19
Energy resolution
- Kα peak and Kβ peak are clearly separated.
- Obtained energy resolution is 6.14 %(FWHM) for Kα peak
- Simulated value is 6.11 % : comparable
TAUP2019
12 Sep 2019
Prototype detector (2) : 180L prototype
- Gas ： Xe 2.3 bar
- Edrift ： 100 V/cm/bar
- EEL ： 3.0 kV/cm/bar
- DAQ time :

## Slide 20
AXEL experiment
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Future prospect
Summary
Contents
TAUP2019
12 Sep 2019

## Slide 21
Future prospect
180L prototype
- Install PMTs
- Increase ELCC unit : 1 → 3 (2019) → 12 (2019) → 27 (2020)
- Enlarged field shaper
- φ15cm, 10cm-long
→ φ40cm, 50cm-long
- Evaluate the performance
using gamma-rays with
511 keV, 622 keV,
1.1 MeV, 1.3 MeV, and
near the Q-value (2.4 MeV)
TAUP2019
12 Sep 2019

## Slide 22
Future prospect
AXEL 3000L
- First physics run with AXEL detector
- First underground detector
- ~φ2m and 1m-long
- Outer detector is used as
active veto
- Aiming to record the world
limit of 0νββ half-life
- Begin to design the concept
TAUP2019
12 Sep 2019

## Slide 23
Future prospect
More ideas…
- Thin, active vessel
- thin : reduce 214Bi
- active : detect α from 214Po
→ can use coincidence of Bi-Po
- candidate :
Polyethylene Napthalate
TAUP2019
12 Sep 2019

## Slide 24
Future prospect
More ideas…
- Positive-Ion Tracking
- electron has a large diffusion constant in xenon gas
- Diffusion constant of xenon ion in xenon gas is much smaller
→ Clear track image
TAUP2019
12 Sep 2019
electron
ion
same event
(simulation)
8
16
24
32
40
48
56
64
time [ms]
ADC ch
Scintillation
xenon ion
Pulse timing (overlaid waveform)
xenon : 1 bar
Wire : φ20 μm
HV : -1500 V
PMT
241Am α-ray source
Wire : -1500V
- Detection of Xe+ by secondary electron
emission at electrode surface

## Slide 25
AXEL experiment
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Future prospect
Summary
Contents
TAUP2019
12 Sep 2019

## Slide 26
AXEL is high pressure gas Xe TPC for 0νββ decay search
- Cellular readout structure (ELCC) is unique feature of AXEL
- Topological information is also used to reject BGs (Deep Learning)
Small (10L) prototype detector has been constructed
- Demonstrate the performance of ELCC
- ⊿ E : 0.82 ~ 1.74 %(FWHM, extrapolated to Q-value) is estimated
Large (180L) prototype detector is now being commissioned
- To demonstrate the performance of AXEL detector at near the Q-value
- Start with a single unit
Aiming to mββ = 20 meV with some ideas
- e.g. Deep leaning, thin (active) vessel, ion tracking
Summary
TAUP2019
12 Sep 2019

## Slide 27
Thank you

## Slide 28
Backup
TAUP2019 at Toyama 12 Sep 2019

## Slide 29
T.Nakadaira
Shuhei Obara
Members
TAUP2019 at Toyama 12 Sep 2019

## Slide 30
Introduction : Neutrinoless Double Beta Decay (0νββ decay)
It occurs only if the neutrino has Majorana mass term
2νββ decay
0νββ decay
If the neutrino is Majorana ……
- naturally explains the smallness of the neutrino mass
- One of the conditions of Leptogenesis story
TAUP2019 at Toyama 12 Sep 2019

## Slide 31
Introduction : Neutrinoless Double Beta Decay (0νββ decay)
Pioneering work by the NEXT experiment group demonstrated usability of high pressure xenon gas time projection chamber (TPC) for 0νββ decay search
Large target mass
Low BG
(BG rejection)
Energy
resolution
To discovery 0νββ decay ……
TAUP2019 at Toyama 12 Sep 2019

## Slide 32
Contents
AXEL experiments
Simulation study
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Summary
TAUP2019 at Toyama 12 Sep 2019

## Slide 33
Simulation study
square
1.0cm
1.0cm
2cm
0.5cm
0.58cm
0.6cm
Edrift=100V/cm/atm
Eanode=3kV/cm/atm
gmsh
elmer
hexagonal
Collection efficiency
of electric field line
is checked by simulation
(gmsh + Elmer)
our design
TAUP2019 at Toyama 12 Sep 2019

## Slide 34
Photon counts
Line of electric field
Electric field strength along the line
(red : EL region)
Electron track by Garfield++
Generate EL lights by MC method
(reflect coefficient of PTFE : 60%)
Simulation study
TAUP2019 at Toyama 12 Sep 2019

## Slide 35
Contents
AXEL experiments
Simulation study
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Summary
TAUP2019 at Toyama 12 Sep 2019

## Slide 36
Gas system
- circulation pump : PumpWorks PW2070
- SEAS micro torr MC1-902FV
- API GETTER-I Re
Prototype detector (1) : 10L prototype
TAUP2019 at Toyama 12 Sep 2019

## Slide 37
XeSAT2018 at Waseda University, 19 Sep 2018
81keV
51keV
30keV
302keV
356keV
326keV
276keV?
272keV?
- Fiducial cut
- Saturated event → cut
- Cell gain calibration
- MPPC saturation correction
etc……
- Gas ： Xe 8 bar
- Edrift ：83 V/cm/bar
- EEL ：2.375 kV/cm/bar
- source : 133Ba
Correction using 30 keV X-ray peak position
30keV
30keV
Details in the next page
Data and Analysis
Prototype detector (1) : 10L prototype

## Slide 38
81keV
51keV
30keV
302keV
356keV
326keV
272keV?
- Fiducial cut
- Saturated events → cut
- Cell gain calibration
- MPPC saturation correction
etc……
- Gas ： Xe 8 bar
- Edrift ：83 V/cm/bar
- EEL ：2.375 kV/cm/bar
- source : 133Ba
Correction using 30 keV X-ray peak position
30keV
30keV
MPPC signal saturate as # of incident photons increases
- saturation curve is characterized by
MPPC recovery time
- measured recovery time one by one
→ apply to
correction
Data and Analysis
two time constants
Schematic of MPPC signal
Voltage
Prototype detector (1) : 10L prototype

## Slide 39
Change the cell pattern
- Cell pattern is changed from square to hexagonal pattern
- More uniform gain is expected since the distance
between neighboring cells becomes same for all channels
Prototype detector (1) : 10L prototype
TAUP2019
12 Sep 2019
7.5mm
13mm
Square pattern
7.5 mm-pitch
Hole : φ5mm
Hexagonal pattern
13 mm-pitch
Hole : φ7mm

## Slide 40
: 0.2 - 0.4
: 0.4 - 0.6
: 0.6 - 0.8
: 0.8 - 1.0
(#Photons in lightest ch) / (Total #photons)
Prototype detector (1) : 10L prototype
TAUP2019
12 Sep 2019
Photon
30keV event
@6bar
Performance with a hexagonal cell pattern
- Energy resolution is worse compared to the square cell pattern
- Dependence of event position was found
- Gas ： Xe 6 bar
- Edrift ： 72 V/cm/bar
- EEL ： 2.25 kV/cm/bar
- source : 133Ba

## Slide 41
Prototype detector (1) : 10L prototype
TAUP2019
12 Sep 2019
Photon
Simulation of the ELCC
- Electron track simulation → Position dependence of EL gain
- Generate 30 keV events by Geant4 → Reproduce EL signal with position dependence
- With these results, configuration of cell is optimized : 10mm-pitch, φ5.5mm
- Compare with data of prototype detector to conform the validity of the simulation
FWHM : 7.5%
Position dependence
Target for 30 keV (4.52%)
w/o any normalization !!!
30keV event
30keV event
EL gain vs Electric field
FWHM
vs Electric field
data1
data2
data2(normalized)
simulation
data1
data2
(13mm-pitch, phi-7mm)
10mm-pitch, phi-5.5mm(simulation)

## Slide 42
Contents
AXEL experiments
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Future prospect
Summary
TAUP2019 at Toyama 12 Sep 2019

## Slide 43
Prototype detector (2) : 180L prototype
- Evaluation of energy resolution near the Q-value
- Concept
Cockcroft-Walton for HV
Readout electronics
ELCC
Field cage
Pressure vessel
TAUP2019 at Toyama 12 Sep 2019

## Slide 44
- Evaluation of energy resolution near the Q-value
- Concept
Cockcroft-Walton for HV
Readout electronics
ELCC
Field cage
Pressure vessel
Prototype detector (2) : 180L prototype
TAUP2019 at Toyama 12 Sep 2019

## Slide 45
Pressure vessel
- SUS304L
- Volume : ~180L (Sensitive Volume : ~100L)
Prototype detector (2) : 180L prototype
TAUP2019 at Toyama 12 Sep 2019

## Slide 46
- Evaluation of energy resolution near the Q-value
- Concept
Cockcroft-Walton for HV
Readout electronics
ELCC
Field cage
Pressure vessel
Prototype detector (2) : 180L prototype
TAUP2019 at Toyama 12 Sep 2019

## Slide 47
ELCC
- Prefabricated style → easily to extend
- Number of channels : ~1000 ch
unit
Prototype detector (2) : 180L prototype
TAUP2019 at Toyama 12 Sep 2019

## Slide 48
- Evaluation of energy resolution near the Q-value
- Concept
Cockcroft-Walton for HV
Readout electronics
ELCC
Field cage
Pressure vessel
Prototype detector (2) : 180L prototype
TAUP2019 at Toyama 12 Sep 2019

## Slide 49
Field cage
- Alignment drift field by strip electrodes
- Reflecting scintillation photons by PTFE
- Withstand discharge structure
- Uniformity of Field strength is checked by FEM simulation
Electrode
PTFE
Insulator
Electric field simulation by FEM
Electric field
Prototype detector (2) : 180L prototype
TAUP2019 at Toyama 12 Sep 2019

## Slide 50
- Evaluation of energy resolution near the Q-value
- Concept
Cockcroft-Walton for HV
Readout electronics
ELCC
Field cage
Pressure vessel
Prototype detector (2) : 180L prototype
TAUP2019 at Toyama 12 Sep 2019

## Slide 51
Introduce low voltage into chamber and boost by Cockcroft-Wakton
inside the chamber to avoid discharge at feedthrough
- Low outgas due to Polyimide
- succeed to generate 10kV with a prototype
Input amplitude : 540 V
Prototype detector (2) : 180L prototype
TAUP2019 at Toyama 12 Sep 2019

## Slide 52
- Evaluation of energy resolution near the Q-value
- Concept
Cockcroft-Walton for HV
Readout electronics
ELCC
Field cage
Pressure vessel
Prototype detector (2) : 180L prototype
TAUP2019 at Toyama 12 Sep 2019

## Slide 53
Readout Electronics
- Readout waveforms of MPPC : 56 ch/board
- Two Flash ADCs to achieve wide dynamic range : 1 p.e ~ 104p.e
- High Voltage supply to MPPCs (in the 0.2mV)
- Monitor MPPC gain constantly
→ adjust (feedback) gain in 0.25% accuracy
- Low cost
Prototype detector (2) : 180L prototype
TAUP2019 at Toyama 12 Sep 2019

## Slide 54
Readout Electronics
- Succeed to readout waveform signals with both of ADCs
Prototype detector (2) : 180L prototype
TAUP2019 at Toyama 12 Sep 2019

## Slide 55
- Construction
TAUP2019
12 Sep 2019
Prototype detector (2) : 180L prototype
Pressure vessel
Feedthrough
FPC

## Slide 56
- Construction
TAUP2019
12 Sep 2019
Prototype detector (2) : 180L prototype
ELCC unit

## Slide 57
- Construction
TAUP2019
12 Sep 2019
Prototype detector (2) : 180L prototype
Anode electrode (ELCC)
Field shaper
-

## Slide 58
Commissioning with a single unit
-
TAUP2019
12 Sep 2019
Prototype detector (2) : 180L prototype
Distribution of dark current charge

## Slide 59
- 3 Units commissioning
- 3.1 bar xenon
- 133Ba source
- 3.0 kV/cm/bar for EL region
TAUP2019
12 Sep 2019
Prototype detector (2) : 180L prototype
After cuts and corrections
now, work in progress
356keV
81keV
30keV
Work in progress

## Slide 60
AXEL experiments
Prototype detector (1) : 10 L prototype
Prototype detector (2) : 180 L prototype
Future prospect
Summary
Contents
TAUP2019 at Toyama 12 Sep 2019

## Slide 61
Future prospect
Sensitivity estimation for 1 ton detector
- Need to reach mββ = 20 meV
- Background free is required
- 214Bi (2447 keV) is serious BG source
- Main source : Pressure vessel (~10 ton)
- Even if we use oxygen-free copper
2.9 ppt 214Bi (cf. EXO-200)
→ 75 event/year for 1 ton detector
arXiv.1502.00581
TAUP2019 at Toyama 12 Sep 2019

## Slide 62
Topological information
- Deep Learning is one of the options
- Learning with simulation of 0νββ and gamma-ray
- Pitch of readout cell is variable to optimization (performance vs costs…)
- Signal efficiency : 41% : BG : 121 evt/yr → 3.2 evt/yr (1 ton Xe)
(assuming 10 tons of pressure vessel made of Oxygen-free Cu, 10mm-pitch readout)
- Estimated sensitivity : mββ = 32 meV (1 ton yr Xe, 10 mm-pitch)
Future prospect
DBD18
21 Oct 2018
signal
Gamma(BG)
model1_02

## Slide 63
Future prospect
Further more…
- Pressurized water shield
- water Cherenkov can be used for muon veto
- thin pressure vessel to reduce mass → reduce 214Bi BG
- Active shield vessel
- detects alpha and beta ray event of 214Bi in the materials of vessel
Polyethylene Naphthalate
TAUP2019 at Toyama 12 Sep 2019