## Slide 1: Temp
Otani
Murakami
2010/8/17
Monte Carlo simulation
Summary of 10a beam DATA
Comparison DATA and MC
Syst. error study

## Slide 2
Overview of MC
2
Component
  Jnubeam 10c (GCOLOR/GFLUKA,nominal beam)-> Estimate Neutrino Flux to INGRID
  NEUT -> Simulate neutrino interaction at the target in INGRID MC
  GEANT4 -> Detector MC

## Slide 3
Updates from last collabo. meeting
3
Reflect Real scintillator demension
Consider interaction vertex in scintillator
  From ratio of scintillator to Fe is about 4~5%
  Use the NEUT file of the Fe target at scintillator vertex (not consider the diff. of cross-section currently).
Add MPPC noise on MC data
Install bad channel
  Not consider the hit at bad channel in MC
Use Jnubeam 10c and weighting with neutrino energy spectrum ratio (FLUKA2008 with real beam)/(Jnubeam 10c with nominal beam).

## Slide 4: Dimension of scintillator bar of MC
The efficient area of a scintillator bar is whole scintillator bar.
In fact, the edge area is reflective material. So the area is not efficient.
Due to this inefficient area, the hit efficiency is dependent on track angle (studied by Christophe, Matsumura-san, Otani-san).
Photo : surface of scintillator bar
white area : the reflective material.

## Slide 5: Weighting with Neutrino energy
Use energy spectrum ratio (FLUKA2008 with real beam) / (Jnubeam 10c with nominal beam) at each energy bin.
  The estimation of FLUKA 2008 is good consistent to NA610-result
  The real beam : accumulated beam parameta @target measured at Run29-34

## Slide 6: Summary of 10a beam DATA
6

## Slide 7
DATA taking efficiency
7
99.9% data taking efficiency (# of good spills = 1005887 / 1006982) Total delivered protons 3.26 x 1019
Summary of # of good spills and protons

## Slide 8
Event selection
8
Make timing cluster(more than 4 hits within 100nsec)
# of active planes > 2 && p.e./active layer > 6.5
Tracking
neutrino event
Track matching
On time
Upstream VETO
Fiducial volume

## Slide 9
Selection efficiency
9

## Slide 10
# of active planes
10

## Slide 11
Vertex X
11

## Slide 12
Vertex Z
12

## Slide 13
Track angle
13

## Slide 14
Accumulated protons and Nobs.
14
Delivered protons ~ 3 x 1019, Total Nobs. ~ 5 x 105

## Slide 15
Event rate stability
15
Event rate is stable within statistical error

## Slide 16
Beam profile
16
Horizontal
Vertical
※statistical error only
※statistical error only
sourth
north
center: 0.1 +- 2.9 cm σ :433 +- 4 cm
center: -10.9 +- 3.2 cm σ :464 +- 6 cm
Run32(April) data
Nobs.
Nobs.
Clear beam profile was observed

## Slide 17
Profile center stability
17
Now we are estimating systematic error
※ Because of mistake with beam line alignment, beam was tuned downward slightly
Horizontal
Vertical

## Slide 18
Selection summary of DATA and MC
18
Comment
MC doesn’t have νe(~1%), νe(~0.1%)
DATA contains many beam-induced events from upstream. (Now we are developing BG MC)
 | DATA(Run29~34) |  | MC(FLUKA2008) |  | MC(GCOLOR) | 
 | # of events | ratio | # of events | ratio | # of events | ratio
protons | 3.26E+19 |  | 1.00E+23 |  | 1.00E+23 | 
# of active plane>2 | 1906146 |  | 2.14E+15 |  | 2.70E+09 | 
p.e./active layer>6.5 | 1906078 | 100.0 | 2.14E+15 | 100.0 | 2.70E+09 | 100.0
tracking | 1804796 | 94.7 | 1.99E+15 | 93.0 | 2.51E+09 | 93.0
track matching | 1749548 | 96.9 | 1.92E+15 | 96.5 | 2.41E+09 | 95.9
on time | 1747181 | 99.9 |  |  |  | 
upstream VETO | 745912 | 42.7 | 1.83E+15 | 95.3 | 2.28E+09 | 94.8
fiducial | 493813 | 66.2 | 1.44E+15 | 78.4 | 1.78E+09 | 78.0
Event rate | 1.51E-14(1.) |  | 1.44E-14(0.95) |  | 1.78E-14(1.18) | 

## Slide 19
MC profile
19
north
south
beam
Horizontal
Vertical
center: 0.5 +- 2.1 cm σ :441 +- 3 cm
center: -5.0 +- 2.2 cm σ :457 +- 4 cm

## Slide 20
Profile X width comparison
20
Jan. and Feb. data set is smaller than MC(~30cm).
Other data set is almost consistent with MC within error.

## Slide 21
Profile Y width comparison
21
Data is larger than MC(~10cm)
~10cm

## Slide 22: Detector syst. error study
22
Results in this talk were obtained with old flux or detector MC. Result will be updated with current flux and detector MC.

## Slide 23
Review: K2K MRD
23
K2K MRD is one of the near detector of K2K
tracker
Iron
Sandwich of tracker and iron
Almost same as INGRID module

## Slide 24
Review: syst. error@K2K MRD
24
“Selection criteria” breakout
For INGRID case, Fiducial volume and difference of start-point(track matching)

## Slide 25
Systematic error of fiducial volume
25
Method
5 additional fiducial volumes are defined and # of events are compared btw DATA(Run29 ~ 34) and MC.
Vertex XY[channel] | Vertex Z[plane#]
2 ~ 21( < 50cm from module center) | 1 ~ 8
3 ~ 20 ( < 45cm ) | 1 ~ 8
4 ~ 19 ( < 40cm ) | 1 ~ 8
2 ~ 21 | 1 ~ 3
2 ~ 21 | 4 ~ 5
2 ~ 21 | 5 ~ 8
nominal
Internal 1
internal 2
upstream
middle
downstream

## Slide 26
Result
26
Module #0
Fiducial volume |  | # of events |  | ratio |  | 
vertex xy[ch] | vertex z[plane] | DATA | MC | DATA | MC | difference
2 ~ 21 | 1 ~ 8 | 25091 | 93802 | 100 | 100 | 0
3 ~ 20 | 1 ~ 8 | 20488 | 76824 | 81.65 | 81.90 | -0.25
4 ~ 19 | 1 ~ 8 | 16451 | 61005 | 65.57 | 65.04 | 0.53
2 ~ 21 | 1 ~ 3 | 8861 | 33536 | 35.32 | 35.75 | -0.44
2 ~ 21 | 4 ~ 5 | 5698 | 21283 | 22.71 | 22.69 | 0.02
2 ~ 21 | 6 ~ 8 | 9416 | 34860 | 37.53 | 37.16 | 0.36
Syst. error |  |  |  |  |  | 0.8
All module case is here

## Slide 27
Syst. error of beam center
27
Compare beam profile(center) with 6 fiducial volumes.
Center = 3.1 +- 1.4 cm
Width = 436 +- 2.3 cm
Center = 3.3 +- 1.5 cm
Width = 434 +- 2.5 cm
You can see all cases here
nominal
internal

## Slide 28
Result
28
Red hatched line : nominal +- 3cm
Almost consistent within error(~3cm)

## Slide 29
Systematic error of track matching selection
29
Method
All the selections except track matching are applied.
And then, track matching selection is applied and # of events is compared btw DATA and MC.

## Slide 30
Δ(vertex Z) after event selection
30
Run32
Nominal selection(-1, 0, +1)

## Slide 31
Estimation of error
31
+0.1% -1.3%
Sys. error =
 | DATA |  | MC |  | 
Δ(diff. Z) | # of events | ratio | # of events | ratio | diff.
-1, 0, +1 | 493812 | 100 | 1267830 | 100 | 0
-2, -1, 0 | 454491 | 92.0 | 1183797 | 93.4 | -1.3
0, +1, +2 | 468334 | 94.8 | 1200552 | 94.7 | 0.1

## Slide 32: x-section and flux syst. error study
32

## Slide 33: Uncertainty of x-section study
Study of the effect from neutrino interaction uncertainties.
Check the difference of # of neutrino observations of INGRID when change # of interactions in module of each interaction.
  ex) # of CCQE interactions × 1.1 → # of observations ?
For check the effect from neutrino interaction uncertainties, not consider the uncertainties of the efficiency of neutrino event selection of INGRID.
This study is about horizontal modules.About vertical modules, we will study in future.

## Slide 34: Result of this study
 | # of observations [/10^14pot] | diff. from original value
CCQE + 10% | 0.813 | +3.7%
CC1Pi + 20% | 0.829 | +5.7%
CC other + 20% | 0.829 | +5.7%
NC + 30% | 0.798 | +1.8%
MC:jnubeam 10ab(250kA), NEUT, INGRID MC (old version at last collabo. meeting)
including numu, numubar, nue, nuebar MC data.
Ex) If CCQE+10% → # of CCQE of numu, numubar, nue, nuebar is increased by 10%.
only about horizontal modules
Original of observations is 0.784 / 10^14 pot

## Slide 35: Effect of hadron production model difference
Check the effect of hadron production model difference.
Hadron production :
  GCALOR/GFLUKA (Jnubeam10b)
  FLUKA
Beam condition : nominal beam
Neutrino cross-section : NEUT model
  cross-section of all interaction mode.
Neutrino selection efficiency : INGRID MC
Only numu, only horizontal modules.
Consider only stat. error.

## Slide 36: Neutrino energy spectrum (Flux)
mod# | 0 | 1 | 2 | 3 | 4 | 5 | 6 | h.mods
Jnubeam10ab | 5.23E+17 | 6.19E+17 | 6.87E+17 | 7.12E+17 | 6.85E+17 | 6.16E+17 | 5.21E+17 | 4.36E+18
FLUKA | 4.82E+17 | 5.61E+17 | 6.18E+17 | 6.39E+17 | 6.19E+17 | 5.62E+17 | 4.82E+17 | 3.96E+18
Diff. [%] | -7.83 | -9.40 | -10.08 | -10.28 | -9.67 | -8.85 | -7.37 | -9.18
Diff. = (FLUKA-10ab)/10ab×100

## Slide 37: Neutrino energy spectrum (Interaction (×cross-section) )
mod# | 0 | 1 | 2 | 3 | 4 | 5 | 6 | h.mods
Jnubeam10ab | 2.39E+06 | 3.14E+06 | 3.66E+06 | 3.84E+06 | 3.66E+06 | 3.13E+06 | 2.38E+06 | 2.22E+07
FLUKA | 1.98E+06 | 2.55E+06 | 2.95E+06 | 3.11E+06 | 2.96E+06 | 2.55E+06 | 1.99E+06 | 1.81E+07
Diff. [%] | -16.92 | -18.80 | -19.28 | -18.90 | -19.07 | -18.60 | -16.47 | -18.46

## Slide 38: Neutrino energy spectrum (observation (× INGRID efficiency) )
mod# | 0 | 1 | 2 | 3 | 4 | 5 | 6 | h.mods
Jnubeam10ab | 7.57E+05 | 1.04E+06 | 1.24E+06 | 1.31E+06 | 1.24E+06 | 1.04E+06 | 7.56E+05 | 7.38E+06
FLUKA | 5.96E+05 | 8.05E+05 | 9.56E+05 | 1.02E+06 | 9.58E+05 | 8.05E+05 | 5.99E+05 | 5.73E+06
Diff. [%] | -21.26 | -22.74 | -22.93 | -22.26 | -22.76 | -22.67 | -20.80 | -22.33

## Slide 39: Beam Profile (observation)
Jnubeam 10ab
FLUKA
 | Beam size (sigma) | Ratio
Jnubeam 10ab | 429±2 cm | 1
FLUKA | 437±2 cm | 1.05
Data | 433±4 cm | 1.01